## Slide 1
EEGNet: Where It Fails, Why, and What To Do About It
A mechanistic failure analysis, a targeted architectural fix, and one underexplored idea
AI Research Engineer — Technical Evaluation · Brainwave Science

## Slide 2
SETUP
Dataset, protocol, and an upfront caveat
PhysioNet EEGBCI — left vs right fist motor imagery, runs 6/10/14 Train: subjects 1–8 Test: subjects 9–10 (held out, per spec) 8–30 Hz band-pass, 128 Hz resample, 2s windows post-cue Fixed seed = 42; 3-seed robustness sweep, best & worst reported
⚠ Data access note
The dev sandbox this repo was built in cannot reach physionet.org (403 on direct request). Code falls back to a synthetic, physiologically-motivated dataset purely to verify the pipeline runs end-to-end. All numbers here are re-run on real data before submission — results.json tags every run with data_source.

## Slide 3
PART 1 — FAILURE ANALYSIS
Where EEGNet breaks: the depthwise spatial filter
Conv2d(F1, F1·D, kernel=(n_channels,1), groups=F1) — one global, fixed linear combination over 64 electrodes, learned once on training subjects, frozen at test time.
1. No transfer pressure
Cross-entropy only needs classes to separate on training subjects. Nothing distinguishes a subject-general filter from one that shortcuts on training-subject-specific geometry.
2. Fixed ≠ personal
Skull thickness, gyral folding, cap offset all shift the electrode-to-source mapping per person. A single global linear filter can't track that.
3. Evidence, not guesswork
Linear probe on penultimate features: subject identity is decodable well above chance from the same representation that fails to generalize class-wise.

## Slide 4
PART 1 — FAILURE ANALYSIS
Three experiments, one embedding check
A
Pooled random split
Subjects 1–8, trials randomly split — optimistic, same-subject leakage
B
Cross-subject
Train 1–8, test 9–10 — the real generalization test
C
Reduced data
3 subjects instead of 8, still tested on 9–10
D
t-SNE / UMAP + linear probe
Does the embedding encode class, subject, or both?

## Slide 5
PART 2 — PROPOSED IMPROVEMENT
Subject-Adversarial EEGNet (SA-EEGNet)
Attach a subject-identity classifier directly to the spatial-filter output, connected through a Gradient Reversal Layer (Ganin & Lempitsky, 2015). Backprop from the subject loss is negated before it reaches the spatial filters — they're trained to keep task signal and actively discard subject identity.
input → temporal conv → spatial filters (bottleneck) → separable conv → task head ↓ GRL (gradient reversed) subject-ID head
Applied at the spatial bottleneck specifically — the exact layer diagnosed in Part 1 — not at the final feature layer (a plain DANN transplant).
What we check (not just accuracy):
• Does subject-decodability at the bottleneck drop toward chance?
• Does class-decodability hold or improve at the same time?
• Does cross-subject test accuracy move relative to the Part 1 baseline?

## Slide 6
PART 3 — ONE THING NOBODY HAS TRIED
State-Conditioned Dynamic Spatial Filtering
Every EEGNet-family model uses a spatial filter that's static per trial. But ERD/ERS is a relative change from a subject's pre-trial idle mu/beta baseline — and that baseline varies trial-to-trial and person-to-person. A fixed filter can't rescale for that.
per-trial mu/beta
band power (FFT)
→
small hyper-
network
→
per-channel
gain (0-2)
→
× base learned
spatial filter
Falsifiable check in the PoC:
• Does the learned gain vector vary meaningfully across trials, or collapse to a constant?
• Does that variation correlate with the band-power state it was conditioned on?
Not claimed: that this beats EEGNet on 10 subjects. That's not a meaningful claim at this scale.

## Slide 7
RESULTS
Best & worst runs across 3 seeds — read from results.json
Experiment | Best | Worst | Notes
A) Pooled random split | [RUN] | — | optimistic, subject leakage
B) Cross-subject baseline | [RUN] | [RUN] | train 1-8 / test 9-10
C) Reduced data (3 subj) | [RUN] | [RUN] | same test set as B
D) SA-EEGNet (Part 2) | [RUN] | [RUN] | compare to B
E) DynamicEEGNet (Part 3) | [RUN] | — | PoC, interpretability check reported separately
[RUN] = fill in from results/results.json after running on real PhysioNet data.

## Slide 8
DEFENCE
Where this could be wrong, and how I'd know
SA-EEGNet underperforms baseline
8 subjects may be too few classes for a stable adversarial gradient — check bottleneck subject-probe accuracy before concluding the idea failed vs. just needs GRL λ warm-up.
Dynamic filter gain collapses to constant
Hypernetwork found it cheaper to ignore state — reported directly via gain_variability, not hidden.
Synthetic vs. real data
Every result is tagged data_source in results.json; synthetic numbers are never reported as findings.
Small test set (2 subjects)
Best/worst across 3 seeds reported throughout — no cherry-picking a single lucky run.

## Slide 9
The mechanism, not the metric
Part 1 diagnoses a specific layer. Part 2 targets that layer directly. Part 3 asks what static filtering assumes and breaks it on purpose.
github.com/<repo> · shgupta@brainwavescience.com